## Slide 1: Speeding up Generalized Fuzzy k-Means Clustering Using m Nearest Cluster Centers Algorithm on GPU
DINH-TRUNG VU (武亭忠)
Department of Computer Science and Engineering
National Taiwan Ocean University
Keelung, Taiwan 202
R. O. C.
利用GPU及m最近群中心加速廣義模糊k均值分群演算法

## Slide 2: Abstract
Implement parallel “Generalized Fuzzy k-Means Clustering Using m Nearest Cluster Centers” (PGFKM) on a GPU
PGFKM algorithm: about 3 to 18 times faster than the optimized CPU code.

## Slide 3: introduction
GFKM: less computing time and better clustering quality than FKM
GFKM running time: grows with the increase of size and dimensionality of data set
Focus on the size of data set.

## Slide 4: organization
PGFKM Model
Updating Membership Step
Calculating New Centroids Step
Checking Convergence Step
Experimental Results.

## Slide 5: PGFKM MODEL
Initialize Centroids
GPU
CPU
Update Membership
Calculate new Centroids
Calculate new Centroids
Check Convergence
Large data set
Small data set
No
Yes
Results
Left small data blocks

## Slide 6: Updating membership on CPU
DNNT : M nearest distances responding to NNTi
For each data point Xi
For each centroid Cj
Update membership for data point Xi
Calculate distance d(Xi, Cj)
Update NNTi and DNNT

## Slide 7: Updating membership on GPU
N data points → N threads working in parallel
Each thread loads the corresponding data point → on-chip registers
Each thread writes < 5 values to shared memory (SM) : use SM broadcast centroids → thread block
Otherwise, threads are read the same centroids in global memory (GM).

## Slide 8: Updating membership on GPU
Thread Ti
i = blockIdx.x * blockDim + threadIdx.x;
For each Cj in GM
Update memberships for Xi
Calculate distance d(Xi, Cj)
Update NNTi and DNNT
Load Xi → on-chip registers
gridDim = N / blockDim

## Slide 9: Updating membership on GPU
Thread Ti
i = blockIdx.x * blockDim + threadIdx.x
For each Cj in SM
Update memberships for Xi
Calculate distance d(Xi, Cj)
Update NNTi and DNNT
Load Xi → on-chip registers
Load centroid
GM → SM → synchronize threads
gridDim = N / blockDim

## Slide 10: Calculating new centroids on CPU
N is small: number of active threads in parallel is small → GPU is inefficient → CPU is still used
The computational complexity : O(NMd + kd).

## Slide 11: Calculating new centroids on CPU
SumUj : sum of memberships of Cj
For each Xi
For each centroid index j in NNTi
Cj = Cj + U’i,jq * Xi
SumUj = SumUj + U’i,jq
For each Cj
Cj = Cj / SumUj

## Slide 12: Calculating new centroids on GPU
N is large, k is close to M : design PGFKM using equation of FKM
The computational complexity : O(Nkd + kd)
Having un-coalesced data access
To achieve coalesced data access, using cuBLAS library:
  transpose data points from N×d to d×N,
  transpose memberships from N×k to k×N.

## Slide 13: Calculating new centroids on GPU
Un-coalesced data access

## Slide 14: Calculating new centroids on GPU
Coalesced data access

## Slide 15: Calculating new centroids on GPU
Reduce Ui,jq for the jth cluster
Reduce Ui,jq * Xi for the jth cluster and the xth dimension.
Executed concurrently or interleaved in six different streams.
Small output block sums: reduced very fast on CPUs.

## Slide 16: Calculating new centroids on GPU
For j = 1 to k
Reduce new centroids
Stream #1 reduces Ui,jq
For x = 1 to d
Stream #(x mod 5 + 1) reduces Ui,jq * Xi
Small block sums
Transpose data points and memberships
CPU
GPU

## Slide 17: Calculating new centroids on GPU
N is relatively large, and k is not close to M : using equation of GFKM
Reduce un-coalesced data accesses : transpose data from N×d to d×N
Reduce un-coalesced membership accesses : sort NNT with keys (cluster indices), values (point indices, memberships).

## Slide 18: Calculating new centroids on GPU
Sorting array NNT has two scenarios :
  (1) using the GPU-based counting sort algorithm
  (2) using the stable sort by keys of Thrust library in CUDA Toolkit
Scenario (1) : the histogram of NNT is calculated first

## Slide 19: Calculating new centroids on GPU
  Histogram write conflicts: a lots of threads with the same cluster index increase the histogram array.

## Slide 20: Calculating new centroids on GPU
Thread Ti
atomicAdd(histogram(NNT(i)), 1)
Thread Ti
idx = atomicAdd(scan(NNT(i)), 1)
sortedMemberships(idx) = U(i)
sortedPointIndices(idx) = i/M
Thread T0
For i = 1 to k
scan(i + 1) = scan(i) + histo(i)
Calculating the histogram of NNT
(gridDim = (N * M) / blockDim)
Calculating the starting index for each cluster
Gathering memberships and point indices
(gridDim = (N * M) / blockDim)

## Slide 21: Calculating new centroids on GPU
Counting sort using atomic functions: not ensure the stability of point indices in each cluster → crossover data accesses of threads reduce performance:

## Slide 22: Calculating new centroids on GPU
Un-crossover data accesses: use the stable sort by keys of Thrust library in CUDA Toolkit.

## Slide 23: Calculating new centroids on GPU
For j = 1 to k
Reduce new centroids
Stream #1 reduces U’i,lq (U’i,lq ∈ cluster #j)
For x = 1 to d
Stream #(x mod 5 + 1) reduces
U’i,lq * Xi (Xi ∈ cluster #j, dimension x)
Small block sums
Transpose data points, sort array NNT, gather memberships and point indices
CPU
GPU

## Slide 24: Checking convergence
Occupies a very small quota → can be designed on CPU or GPU
On GPU:
  each thread executes one dimensional of centroid
  each thread block executes for one centroid.

## Slide 25: Experimental Results
Performance measure :
  CUDA version 7.0 : 64 bit
  NVIDIA GeForce GTX 760 GPU : six SIMD multi-processors × 192, 1.5 GHz, 2GB, 192.2 GB/s
  Intel(R) Core(TM) i5-4690 CPU : four core, 3.5 GHz, 8GB, 25.6 GB/s

## Slide 26: Experimental Results
Four version:
  Version 1 : calculating new centroids on CPU
  Version 2 : calculating new centroids on GPU using equation of FKM
  Version 3 : calculating new centroids on GPU using counting sort
  Version 4 : calculating new centroids on GPU using Thrust stable sort by key

## Slide 27: Experimental Results
First test on a real data set from three real images: “Lena,” “Baboon,” and “Peppers,” : N = 49,152, d = 16, M = 2, k = 8, and ε = 1e-8.
GFKM method | Speedup of PGFKM |  |  | 
 | Version 1 | Version 2 | Version 3 | Version 4
Updating memberships | 10.5 | 9.95 | 11.38 | 11.41
Calculating new centroids | 1.14 | 1.35 | 1.52 | 0.98
Checking convergence | 0.00 | 0.00 | 0.00 | 0.00
Total after 200 iterations | 6.14 | 6.40 | 7.32 | 5.92

## Slide 28: Experimental Results
Second test shows the changing speedup with various N on the “poker” data set : d = 10, M = 2, k = 10, ε = 1e-8, max iterations = 200.