## Slide 1: Speeding up Generalized Fuzzy k-Means Clustering Using m Nearest Cluster Centers Algorithm on GPU
Student：Dinh-Trung Vu
Advisor：Prof. Zone-Chang Lai

## Slide 2: OUTlINE
Introduction
Parallel GFKM model
Updating membership step
Calculating new centroids step
Checking convergence step
Experimental results
Conclusion and Future work

## Slide 3: introduction
GFKM: less computing time, better clustering quality than FKM,
The optimal value of M is 2 → the better clustering results,
Size, dimensionality grow → GFKM’s running time grows,
Focus on the size of data set,
Implement parallel GFKM (PGFKM) on a GPU,
PGFKM : 3 to 18 times faster than the optimized CPU code.
Notes: Average speedup is about seven to ten times

## Slide 4: OUTlINE
Introduction
Parallel GFKM model
Updating membership step
Calculating new centroids step
Checking convergence step
Experimental results
Conclusion and Future work

## Slide 5: Parallel GFKM Model
Initialize Centroids
GPU
CPU
Update Membership
Calculate new Centroids
Calculate new Centroids
Check Convergence
Large data set
Small data set
No
Yes
Results
Left small data blocks

## Slide 6: OUTlINE
Introduction
Parallel GFKM model
Updating membership step
Calculating new centroids step
Checking convergence step
Experimental results
Conclusion and Future work

## Slide 7: Updating membership on CPU
DNNT : M nearest distances responding to NNTi
For each data point Xi
For each centroid Cj
Update membership for data point Xi
Calculate distance d(Xi, Cj)
Update NNTi and DNNT
Two levels of loop

## Slide 8: Updating membership on GPU
One level of loop : N threads in parallel
Each thread :
  loads a data point → on-chip registers,
  reads same centroids in shared memory :
  writes < 5 values → shared memory, else
  reads same centroids in global memory.

## Slide 9: OUTlINE
Introduction
Parallel GFKM model
Updating membership step
Calculating new centroids step
Checking convergence step
Experimental results
Conclusion and Future work

## Slide 10: Calculating new centroids on CPU
Number of data points N is small :
Number of active threads in parallel is small
→ GPU is inefficient → CPU is still used,
The computational complexity : O(NMd + kd).

## Slide 11: Calculating new centroids on GPU
N is large, k is close to M : using equation of FKM,
The computational complexity : O(Nkd + kd),
Have un-coalesced data access,
To achieve coalesced data access, use cuBLAS to :
  transpose data points from N×d to d×N,
  transpose memberships from N×k to k×N.

## Slide 12: Calculating new centroids on GPU
Un-coalesced data access

## Slide 13: Calculating new centroids on GPU
Coalesced data access

## Slide 14: Calculating new centroids on GPU
Reduce Ui,jq for the jth cluster,
Reduce Ui,jq * Xi for the jth cluster and xth dimension,
Executed concurrently or interleaved
in six different streams,
Small output block sums are reduced very fast on CPUs.

## Slide 15: Calculating new centroids on GPU
N is large, k is not close to M : using equation of GFKM,
The computational complexity : O(NMd + kd),
Reduce un-coalesced data accesses :
Transpose data points from N×d to d×N.
Reduce un-coalesced membership accesses : sort NNT
  keys : cluster indices,
  values : point indices, memberships.

## Slide 16: Calculating new centroids on GPU
Sorting NNT has two scenarios :
  (1) using GPU-based counting sort algorithm,
  (2) using stable sort by keys of Thrust library.
Scenario (1) : histogram of NNT is calculated first.

## Slide 17: Calculating new centroids on GPU
  Histogram write conflicts : a lots of threads with the same cluster index increase the histogram array

## Slide 18: Calculating new centroids on GPU
Thread Ti
atomicAdd(histogram(NNT(i)), 1)
Thread Ti
idx = atomicAdd(scan(NNT(i)), 1)
sortedMemberships(idx) = U(i)
sortedPointIndices(idx) = i/M
Thread T0
For i = 1 to k
scan(i + 1) = scan(i) + histo(i)
Calculating histogram of NNT
(gridDim = (N * M) / blockDim)
Calculating starting index for each cluster
Gathering memberships and point indices
(gridDim = (N * M) / blockDim)
Counting sort using atomic functions

## Slide 19: Calculating new centroids on GPU
Counting sort using atomic functions :
not ensure the stability of point indices in one cluster
→ crossover data accesses reduce performance.

## Slide 20: Calculating new centroids on GPU
Un-crossover data accesses :
Use stable sort by keys of Thrust library.

## Slide 21: Calculating new centroids on GPU
Reduce U’i,lq for the jth cluster,
Reduce U’i,lq * Xi for the jth cluster and xth dimension,
Executed concurrently or interleaved
in six different streams,
Small output block sums are reduced very fast on CPUs.

## Slide 22: OUTlINE
Introduction
PGFKM model
Updating membership step
Calculating new centroids step
Checking convergence step
Experimental results
Conclusion and Future work

## Slide 23: Checking convergence
Occupying a very small quota → on CPU or GPU,
On GPU:
  each thread executes one dimensional of centroid,
  each thread block executes one centroid.

## Slide 24: OUTlINE
Introduction
PGFKM model
Updating membership step
Calculating new centroids step
Checking convergence step
Experimental results
Conclusion and Future work

## Slide 25: Experimental Results
  CUDA version 7.0 : 64 bit
  NVIDIA GeForce GTX 760 GPU :
    six multi-processors × 192 = 1152 cores,
    0.980 GHz, 2GB, 192.2 GB/s.
  Intel(R) Core(TM) i5-4690 CPU :
    four cores,
    3.5 GHz, 8GB, 25.6 GB/s.

## Slide 26: Experimental Results
  Four versions for calculating new centroids step:
    Version 1 : on CPU,
    Version 2 : on GPU using equation of FKM,
    Version 3 : on GPU using counting sort,
    Version 4 : on GPU using Thrust stable sort by key.

## Slide 27: Experimental Results
First test : speedup on a real medium data set :
“Lena,” “Baboon,” and “Peppers” with N = 49152, d = 16.
GFKM method M = 2, k = 8, ε = 1e-8 | Speedup of PGFKM |  |  | 
 | Version 1 | Version 2 | Version 3 | Version 4
Updating memberships | 10.5 | 9.95 | 11.38 | 11.41
Calculating new centroids | 1.14 | 1.35 | 1.52 | 0.98
Checking convergence | 1.00 | 1.00 | 1.00 | 1.00
Total after 200 iterations | 6.14 | 6.40 | 7.32 | 5.92

## Slide 28: Experimental Results
Second test : changing speedup with various N on “poker” data set with d = 10, M = 2, k = 10, ε = 1e-8, and maximum iterations = 200.

## Slide 29: Experimental Results
Third test : changing speedup with various k on “poker” data set with N = 1025100, d = 10, M = 2, ε = 1e-8, maximum iterations = 200.

## Slide 30: Experimental Results
Fourth test : changing speedup with various d on “Synthetic” data set with N = 491520, M = 2, k = 8, ε = 1e-8, and maximum iterations = 200.

## Slide 31: OUTlINE
Introduction
PGFKM model
Updating membership step
Calculating new centroids step
Checking convergence step
Experimental results
Conclusion and Future work

## Slide 32: Conclusion and future work
The better speedups : larger N, smaller d and k
High-dimensional : data point cannot be loaded into registers → reduce performance
In future, calculate temporary distance, store in on-chip registers :
  load the data → shared memory, tile by tile,
  adopt the idea of parallel matrix multiplication.
Notes: Average speedup is about seven to ten times

## Slide 34
Thank You